## Slide 1
MOOC 2
Energy transition measurement and monitoring tools

## Slide 2
Course Index
UNIT 1: INTRODUCTION
UNIT 2: PARTICULARITIES OF TOURIST ISLANDS
UNIT 3: AVAILABLE TYPES OF ENERGY PLANNING AND MONITORING TOOLS
UNIT 4: GENERA TOOLS: ENERGY PLANNING
UNIT 5: GENERA TOOLS:
STRATEGY EVALUATION
UNIT 6: CASES STUDY USING THE GENERA MONITORING TOOL

## Slide 3
UNIT 1
INTRODUCTION
MOOC 2: Energy transition measurement and monitoring tools
3

## Slide 4
UNIT 1. INTRODUCTION
INDEX
1
Evolution of the energy transition
2
Regional overview
3
Decision support models
4

## Slide 5
1.1 Evolution of the energy transition
Policymakers face two challenges inherent in the energy transition: what is needed to accelerate the improvement of energy systems, and what should be the conditions necessary to take advantage of the transition's emerging opportunities? The evaluation of a country's energy system performance revolves around these three key premises. Balancing these aspects is crucial for a successful energy transition.
Security
Ensure security of supply through the energy mix, trading partners and electricity generation.
Equity
Ensure fair distribution, accessibility and affordability of energy for everyone.
Sustainability
Incorporate metrics to reduce carbon intensity, improve efficiency, and promote renewable energy sources.
5

## Slide 6
1.2 Regional overview
Prioritize Equity
Address disparities in equity, which represent the most significant divergence in system performance between advanced economies and emerging nations.
Reduce Regulatory Disparity
Work towards reducing the regulatory gap between regions with advanced economies and those that are developing.
Balance Equity and Sustainability
Address the global imperative to balance equitable transition with decarbonization efforts.
6

## Slide 7
Analytical Role
Analyze the feasibility, costs, and impacts of different energy transition routes. Provide information on technology deployment, policy implications, and socio-economic factors.
Integrated Assessment
Combine information from different scientific disciplines to provide a comprehensive view of global environmental change and sustainable development.
Quantitative Description
Offer a quantitative description of processes and interactions in the energy system, enabling policymakers to make informed decisions.
1.3 Decision Support Models
Nowadays, decision making mainly in the environmental field requires information from different scientific disciplines and this gives rise to integrated assessment models.
The main objective of integrated assessment models is to provide a political view of global environmental change and sustainable development through a quantitative description of processes and interactions.
7

## Slide 8
Modeling Approach for Integrated Assessment Systems
Define Scope
Determine the sectors of the economy and focal points to be included in the model.
Select Methodology
Choose between general equilibrium and partial equilibrium models based on the complexity required.
Gather Data
Collect relevant data on energy production, consumption, and environmental impacts.
Develop Scenarios
Create various scenarios to explore different policy options and their potential outcomes.
1.3 Decision Support Models
8

## Slide 9
Challenges in Modeling Integrated Assessment Systems
Data and Uncertainty
High levels of uncertainty due to hard-to-access data and assumptions about future technological advances, political decisions, and social behavior.
Intermittency and Storage
Modeling the intermittency of renewable sources and advances in energy storage technologies requires sophisticated algorithms.
Regional Differences
Systems must consider regional variations in renewable resource availability, energy demand, and infrastructure.
Socioeconomic Factors
Incorporating social, political, and behavioral factors that are difficult to quantify but crucial for a comprehensive analysis.
1.3 Decision Support Models
9

## Slide 10
UNIT 2
PARTICULARITIES OF TOURIST ISLANDS
MOOC 2: Energy transition measurement and monitoring tools
10

## Slide 11
UNIT 2. PARTICULARITIES OF TOURIST ISLANDS
1
Importance of island regions
2
Challenges specific to tourist islands
3
Use of energy in isolated microgrids
4
Renewable islands
INDEX
11

## Slide 12
Importance of Island Regions
EU islands offer unique opportunities for modern energy planning, with potential for energy efficiency, renewable energy, and innovative solutions. Their small size and remoteness make them ideal testbeds for energy autonomy.
Specific Challenges
Islands face challenges such as land scarcity, climate risks, high seasonality of demand, isolation, and data scarcity. These factors complicate energy planning and require tailored solutions.
Energy in Isolated Microgrids
Microgrids offer potential solutions for electrifying remote areas, supporting isolated regions energetically, and facilitating the integration of renewable energy sources.
2.1 Importance of island regions
12

## Slide 13
2.2 Challenges specific to tourist islands
13
Land Scarcity
Limited space for renewable energy deployment. Solutions include offshore floating photovoltaics, rooftop solar, offshore wind, and innovative technologies like vertical photovoltaics and agrivoltaics.
Climate Risks
Islands are particularly vulnerable to climate change impacts. Incorporating distributed energy systems and storm-resistant technologies can enhance system resilience.
High Seasonality
Tourism-driven demand fluctuations require comprehensive seasonal storage solutions and explicit demand modeling beyond typical continental load curves.
Isolation and Data Scarcity
System stability issues and lack of data affect demand forecasting. Solutions include physical connections to neighboring systems and use of global demand databases.

## Slide 14
2.3 Use of energy in isolated microgrids
14
Definition
Interconnected energy system operating as a controllable entity within defined electrical boundaries
Objectives
Support isolated areas, integrate renewable sources, reduce emissions
Challenges
Complex optimization needed to manage renewable uncertainty and maintain service quality
The adoption of isolated microgrids remains limited due to the uncertainty produced by renewables and intrinsic load demand. Therefore, the use of intermittent energy resources along with conventional ones could resolve the uncertainty.
It is of utmost importance to incorporate efficient optimization strategies that reduce energy costs, pollution, fuel consumption, etc. and ensure the highest quality of service.
Optimization strategies are a complex process involving different variables such as the time frame, the existing constraints, the objective function, the optimization framework, the treatment of uncertainty or the optimization algorithm.

## Slide 15
Time Frame
Consider the time horizon and resolution time of the optimization algorithm.
Constraints
Address technical, environmental, and logical constraints specific to isolated microgrids.
Objective Function
Define the function to be optimized, typically involving minimization of network costs and pollutant emissions.
Optimization Framework
Choose between centralized, decentralized, or distributed architectures for information processing.
2.3 Use of energy in isolated microgrids
15

## Slide 16
Ameland, Netherlands
Installed a 23,000-panel solar park in 2015, producing enough electricity for 1,500 households annually. The community plays a key role in developing a holistic and sustainable energy vision.
Menorca, Spain
Plans to increase renewable generation to 85% of electricity consumption by 2030, reduce fossil fuel use by 50% for transportation and 30% for buildings. High environmental awareness drives the transition.
2.4 Renewable islands
16

## Slide 17
Tilos, Greece
The local community and City Council are motivated to undertake a deeper energy transition, including clean electromobility and the development of a prosumer cluster on the island. Plans include increased automation and flexibility of the local electricity distribution network, showcasing the potential for small islands to lead in renewable energy adoption.
Pantelleria, Italy
As it is not connected to the national grid, the island's electricity is produced locally in a 22 MW diesel power plant.
Focusing on electrifying local public transportation, including a large photovoltaic system to cover 100% of electric bus consumption annually.
2.4 Renewable islands

## Slide 18
UNIT 3
AVAILABLE TYPES OF ENERGY PLANNING AND MONITORING TOOLS
MOOC 2: Energy transition measurement and monitoring tools
18

## Slide 19
UNIT 3. AVAILABLE TYPES OF ENERGY
PLANNING AND MONITORING TOOLS
INDEX
1
Integrated Assessment Models (IAMs)
2
Available Tools
3
Challenges for Tool Improvement
19

## Slide 20
Scope
Cover multiple sectors of the economy and focal points, addressing the multidisciplinary nature of energy transition challenges.
Program
Consider programming and software requirements for implementing and running the models.
Economic Complexity
Choose between general equilibrium and partial equilibrium models based on the level of detail and interactions required.
3.1 Integrated Assessment Models (IAMs)
As discussed in Unit 1, Integrated Assessment Models are very useful for addressing societal challenges, specifically those related to environmental policy and the path towards decarbonization.
20

## Slide 21
Cooperative
The output of one model is used as input to another model, creating a chain of analysis.
Complementary
Two or more models work together to achieve a result, with each model being essential to the overall analysis.
Independent
Models create their own results independently, but can be merged to provide a more comprehensive analysis.
Understanding these synergies is crucial for developing holistic approaches to decarbonization pathways and associated socioeconomic narratives.
There are three main types of synergies:
3.1 Integrated Assessment Models (IAMs)
21

## Slide 22
Significant IAMs for Energy Transition
G4M (Global Forest Model)
Compares income from forests with potential income from alternative land uses, such as growing food grains or biofuels.
IBC (Integrated Benefits Calculator)
Converts LEAP emissions scenarios into estimates of health problems, ecosystem impacts, and climate impacts.
PRIMES
Simulates energy consumption and supply in the European Union, modeling energy market equilibrium for each member state.
3.1 Integrated Assessment Models (IAMs)
22

## Slide 23
SAP Temperature Calculator
Purpose
Calculates annual temperature changes based on input of all relevant emissions affecting temperature.
Features
Shows the degree of influence of different warming and cooling substances over time. Uses globally averaged coefficients for temperature change calculations.
Application
Useful for quick assessments of emission scenarios and their potential temperature impacts.
3.2 Available Tools
23

## Slide 24
Description
LEAP-IBC (Long-range Energy Alternatives Planning system - Integrated Benefits Calculator) is an integrated modeling and scenario planning tool for energy and greenhouse gas planning.
Key Features
Considers the location of emissions, which significantly affects the temperature impact at different points on the globe. Useful for quantifying the impact of various existing plans.
Limitations
Requires an elaborate database on the study site and a medium level of knowledge from users.
3.2 Available Tools
LEAP-IBC
24

## Slide 25
Purpose
Specifically designed to increase the integration of Renewable Energy Sources (RES) in stand-alone systems. Used as a planning tool for individual energy systems.
Advantages
Tailored for island systems, offering detailed analysis of renewable integration in isolated grids.
Limitations
Not sold to external users, requires up to two months of training, and has limited accessibility due to its complexity.
3.2 Available Tools
H2RES
25

## Slide 26
GAINS
Greenhouse Gas – Air Pollution Interactions And Synergies assesses GHG and air pollutant emissions from main emitting sectors. It evaluates the effect of different emission control strategies.
SWEET
Solid Waste Estimation Tool quantifies GHG emissions and other air pollutants from the municipal solid waste sector. It can estimate historical emissions and assess impacts of waste sector policies.
3.2 Available Tools
Roadmap Model
Developed by ICCT, it estimates GHG emissions and pollutants from road transport. Useful for developing historical inventories and projecting future emissions under different policy scenarios.
A simulation model for evaluating different energy system alternatives. Free to download but requires expert knowledge. Assists in designing national or regional energy planning strategies.
EnergyPlan
26

## Slide 27
Generic Guidelines
Existing tools offer guidance to policymakers, but provide very generic guidelines that may not offer concrete solutions.
Lack of Regional Specificity
Many tools do not integrate data specific to certain regions, such as islands, limiting their applicability in these contexts.
Technical Complexity
Use is often limited to personnel with technical knowledge, making them less accessible to policymakers.
Monitoring Limitations
Difficulty in easily monitoring progress towards energy transition goals, as tools often only provide quantifiable scenarios or results for different strategies.
3.3 Challenges for Tool Improvement
27
In short, the creation of a CETA or SECAP is necessary to achieve the objectives set by the EU, for this the use of some tools acquires a fundamental role. In this unit we have reviewed some of them, and we have also identified some of the challenges that need to be addressed so that the energy transition can be tackled from the municipal level:

## Slide 28
Objective
GENERA aims to help public authorities transform the energy context of European regions to facilitate a rapid transition to a decarbonized and sustainable economy.
Focus Areas
EU and island energy context, identification of existing monitoring tools, key players and stakeholders, financial mechanisms, and best practices at the municipal level.
Approach
Provide municipalities with simple and accessible Energy Transition monitoring tools for all interested parties, addressing the limitations of existing tools.
3.3 Challenges for Tool Improvement
GENERA PROJECT
Identification of existing monitoring tools
Financial mechanisms
Identification of key players and stakeholders
EU and island energy context: Canary, Balearic, Greek and Italian islands
Raising awareness of the energy transition
Best practices applied at the municipal level
28

## Slide 29
The GENERA project proposes to provide municipalities with simple and accessible ET monitoring tools for all interested parties:
Monitor their progress towards established commitments (such as the Covenant of Mayors).
Create a knowledge database integrating holistic information related to ET (specifically in Mediterranean islands).
Provide a package of specific energy solutions for tourist islands, transforming information into added value for policy and decision makers.
Introduce a co-creation approach to the decision making process by using a multi-criteria methodology for identifying the most promising solution.
3.3 Challenges for Tool Improvement
GENERA PROJECT

## Slide 30
UNIT 4
GENERA TOOLS:
ENERGY PLANNING
MOOC 2: Energy transition measurement and monitoring tools
30

## Slide 31
31
UNIT 4. GENERA TOOLS:
ENERGY PLANNING
INDEX
1
Objectives of the energy planning module
2
Features
3
Indicators
4
Tool sections
5
Application example

## Slide 32
Objectives of the GENERA Project
Business As Usual (BAU) Scenario
Analyze the current scenario and its evolution over the considered time interval as a reference point.
Alternative Scenarios
Compare alternative energy scenarios with the same time horizon and demand constraints to explore different transition pathways.
Comparative Analysis
Provide insights into the potential outcomes of different energy strategies and policy decisions.
4.1 Objectives of the Energy Planning Module
32

## Slide 33
Scenario Evaluation
Assess and optimally match energy sources and their conversion to the energy needs of different demand sectors (commercial, industrial, residential, etc.).
Annual Rate Projections
Use annual rates of change to define the energy demand of each sector over time.
Comparative Analysis
Compare the BAU scenario with an Energy Transition (ET) scenario based on renewable energy and policy-driven sustainability goals.
Macro-level Insights
Provide a macro-level comparison between scenarios to inform high-level decision-making.
4.2 Features
33

## Slide 34
Primary Indicators
Primary energy demand by energy source
Electricity generation by each energy source
Total CO2 emissions from each energy sector
Secondary Indicators
Percentage of foreign dependence on primary energy supply
Percentage of renewable energies in total energy consumption
Energy intensity (ratio of energy consumption to GDP)
4.3 Key Indicators
34

## Slide 35
Introduction
Brief explanation of the tool's contents and purpose
Growth Rates
Calculation of growth ratios used for estimations
Auxiliar
Data entry from external sources (e.g., IEA database)
ESC-BAU
Calculation of Business-As-Usual scenario and future trends
ESC-ET
Calculation of Energy Transition scenario with new projections
4.4 Tool sections
35

## Slide 36
Recommended Database
The tool is adapted to use information from the IEA's "World Energy Balances Highlights" database.
Data Selection
Use the latest year containing the most complete information possible for accurate analysis.
Importance
Reliable and standardized data ensures consistency and comparability in energy planning across different regions.
4.4 Tool sections

## Slide 37
Growth Rates
Data Input
Enter total energy consumed by each sector for the last reference year from the IEA database. Include recent population and Gross Domestic Product data for the country under study.
Calculation
Growth rates are calculated based on the last year entered in the tool, providing a basis for future projections.
Importance
Accurate growth rates are crucial for realistic scenario modeling and energy demand forecasting.
4.4 Tool sections
37

## Slide 38
Energy Sources
Enter information for each energy source: coal, crude oil, oil products, natural gas, nuclear, renewables, biofuels, electricity, and heat energy vectors.
Sector Contribution
Input each source's contribution to different sectors: industry, transportation, residential, commercial, and others.
Unit Conversion
Data is provided in PJ but must be converted to kteps. The tool includes auxiliary sheets for automatic conversion.
4.4 Tool sections
Auxiliary Section: Data Entry
38

## Slide 39
4.4 Tool sections
Auxiliary Section: Data Entry
39

## Slide 40
4.4 Tool sections
Auxiliary Section: Data Entry
40

## Slide 41
ESC-BAU
Inputs Section
Assumptions are made and input data is automatically entered from pre-filled sheets (growth rates and auxiliary).
Outputs Section
Automatically calculates estimates for future years. Provides evolution of growth rates, energy source contributions to each sector, and emissions produced.
Time Frame
Years can be entered manually or automatically, allowing for flexible scenario planning.
4.4 Tool sections
41

## Slide 42
ESC-BAU
42
4.4 Tool sections
INPUTS
OUTPUTS

## Slide 43
ESC-BAU: Results Visualization
43
4.4 Tool sections
Energy Demand Projection
Visualizes the projected energy demand over time for different sectors.
Electricity Generation Mix
Illustrates the projected electricity generation by source over the years.
CO2 Emissions Trend
Shows the projected CO2 emissions from different energy sectors over time.

## Slide 44
Purpose
Provides a comprehensive overview of the country's energy context in the Business-As-Usual scenario.
Content
Illustrates the contribution of each energy source to each sector, showing the conversion of primary energy to final energy.
Utility
Helps visualize the current energy flow and identify areas for potential improvement in the energy transition process.
4.4 Tool sections
ESC-BAU: BAU Diagram
44

## Slide 45
4.4 Tool sections
ESC-ET
Purpose
Models an energy transition scenario proposing sustainable improvements for the country.
Inputs Section
Allows modification of previously established assumptions to create different transition scenarios.
Outputs Section
Can be modified according to the criteria deemed necessary for the specific ET scenario being evaluated.
45

## Slide 46
4.4 Tool sections
ESC-ET
Shows the input fields for modifying assumptions in the Energy Transition scenario.
Displays the calculated results based on the modified assumptions for the ET scenario.
INPUTS
OUTPUTS
46

## Slide 47
4.4 Tool sections
ESC-ET: Results Visualization
ET Energy Demand
Visualizes the projected energy demand in the Energy Transition scenario.
ET Electricity Mix
Illustrates the projected electricity generation mix in the Energy Transition scenario.
ET CO2 Emissions
Shows the projected CO2 emissions trend in the Energy Transition scenario.
47

## Slide 48
Hypothesis
Introduce a 2% annual substitution of oil by biofuels in the energy mix.
Implementation
Modify the output section formulation to reduce oil use for fuel and replace it with renewable sources.
Goal
Demonstrate how small changes in energy policy can impact the overall energy transition scenario.
4.5 Application example
It is proposed as an example to create an energy transition scenario for Spain in which the following hypothesis is introduced:
48

## Slide 49
4.5 Application example
Therefore, the following equations must be entered for each year of calculation in the outputs section.
49

## Slide 50
4.5 Application example
50
Energy Mix Comparison
Visualizes the difference in energy mix between the Business As Usual and Energy Transition scenarios.
Emissions Reduction
Illustrates the potential reduction in emissions achieved through the Energy Transition scenario.

## Slide 51
1
Scenario Comparison
The tool enables a clear comparison between Business As Usual and Energy Transition scenarios, highlighting potential benefits of policy changes.
2
Flexibility
Users can easily modify assumptions and inputs to model various energy transition strategies and their impacts.
3
Comprehensive Analysis
The tool provides insights into energy demand, electricity generation mix, and CO2 emissions, offering a holistic view of the energy system.
4
Decision Support
By visualizing potential outcomes, the tool aids policymakers in making informed decisions about energy transition strategies.
Key Takeaways from the Energy
Planning Module
51

## Slide 52
UNIT 5
GENERA TOOLS:
STRATEGY EVALUATION
MOOC 2: Energy transition measurement and monitoring tools
52

## Slide 53
UNIT 5. GENERA TOOLS:
STRATEGY EVALUATION
1
Strategy evaluation method
2
Calculation tool
3
Strategy evaluation tool
4
Selection of the most promising energy policies
INDEX
53

## Slide 54
Purpose
This unit focuses on tools and methodologies for evaluating different energy transition strategies using the GENERA framework.
Key Components
Not only are the technical or economic parameters of the implementation of sustainability-related measures, such as photovoltaic solar energy in isolated communities, considered, but also the environmental, social and political variables involved in the final decision
Outcome
The Analytical Hierarchical Process (AHP) method is proposed to be used to obtain the solutions that best meet the municipal needs. Participants will learn how to effectively compare and evaluate various energy transition pathways to inform policy decisions.
5.1 Strategy evaluation method
54

## Slide 55
5.1 Strategy evaluation method
55
The method proposed by the GENERA project consists of facilitating training in quantitative energy terms (calculation of energy saved per measure and CO2 emissions mitigated), as well as providing training in the use of multi-criteria techniques that allow the joint evaluation of quantitative and qualitative aspects.
Method
1. Calculation Module
2. Strategy evaluation module
Actions to be included in the action plan
Quantitative results
Provides technical information to policymakers
Qualitative and quantitative evaluation of actions
Ranking of the most promising measures

## Slide 56
5.1 Strategy evaluation method
56
Representing the problem in a hierarchical structure allows to get an overview of the whole process and at the same time to analyze whether the model adequately represents the relative magnitude of each criterion.
2. Strategy evaluation module
Level 1: in reference to the different areas that affect the municipal level.
Level 3: each of the strategies is evaluated according to the previous levels.
Level 2: the indicators that affect each level.

## Slide 57
5.2 Calculation Tool
57
Tool implemented in excel spreadsheet that allows to calculate emission and energy savings for certain measures of municipal interest, performing the calculations based on the information provided by the user. The more information, the more it adapts to the municipality of analysis.
Method
Municipal Buildings and Public Facilities: This section includes all actions related to municipal buildings and equipment under the responsibility of the city council.
Transport: This section includes information and actions related to the improvement of transport at municipal level.
Industry: This section includes all industry-related actions and an incentive programme for energy saving and efficiency and the use of renewable energy in housing and SMEs. This section has the aim of reducing final energy consumption and CO2 emissions
Awareness: This section includes information and actions related to recycling and environmental awareness of citizens

## Slide 58
5.2 Calculation Tool
58
Municipal Buildings and Public Facilities
Industry
Input Data
Window’s materials and isolation
Nº of Bulbs and replacements
Heating and cooling Demand
Type of heating/cooling systems, Fuel, Equipment available, coolant, fans etc.
Annual Electrical Demand: type of building, Surface, DHW Demand etc.
RE Available and technologies
Vehicles to replace with EV
Incentive lines depending on the industry sector
Actions to be implementend througout the sector: equipment, efficiency, energy generation, type of process etc.

## Slide 59
5.2 Calculation Tool
59
Transport
Awareness
Input Data
Inhabitants
Distance of the cycleway to be builted-up
Nº of EV Chargers and power
Measures related to promotion of public transport: speed zones, fees, tolls etc.
Inhabitants
Awareness plan
Events: school, associations, citizens etc.
Recycling points
Bonuses for self-consumption

## Slide 60
5.2 Calculation Tool
60
Results
For each action is obtained:
  Energy Savings (kWh/year)
  CO2 emissions saved (kgCO2 eq)
  The results will be used as quantitative information for the next module.

## Slide 61
Tool
Features
Free software
Allows you to easily define the elements, their relationships, enter the importance of the relationships and obtain the results.
The program is implemented in Spanish and English, selectable from the menu
5.3 Strategy evaluation tool
61
As a support tool, the “Super Decisions” software is used as a decision support method that implements the AHP. The objective would be to achieve a planning of measures according to the municipal casuistry.

## Slide 62
5.3 Strategy evaluation tool
62
Indicator | Criteria to which it applies
Maturity | 
Municipal RE Share (%) | 
Annual Energy Savings (MWh) | 
Annual RE Production (MWh) | 
Implementation Rate | 
Investment | 
Annual Profitability (kWh/€) | 
Available Funding and Grants | 
Public Acceptance | 
Job Creation | 
CO2 Emissions Reduction (tCO2) | 
Biodiversity Impact | 
Land Change of Use | 
Political Acceptance | 
Compatibility with national Policies | 
Compatibility with regional Policies | 
Compatibility with EU Policies | 
Technical
Ecological impact
Economic
Social
Political
Level 1 and 2 are entered into the tool, and the corresponding connections are made between them according to the following table.

## Slide 63
5.3 Strategy evaluation tool
63
Each of the indicators should be evaluated and weighted according to the relative importance of each criterion (technical, ecological, social, economic and political impact).
Evaluation
Weighting
For this purpose, weights (from 1 to 10) are assigned to each of the indicators.
The same procedure is carried out for each of the alternatives or proposed actions.
Procedure

## Slide 64
5.4 Selection of the most promising energy policies
64
After performing the simulation or synthesizing the whole model, the results will be obtained for each of the alternatives or actions in this case.
The Normal column presents the results in the form of priorities. This is the usual way of reporting the results.
The Ideals column is derived from the Normals column by dividing each of its entries by the highest value in the column.
The ranking column shows the final result of the order of alternatives.

## Slide 65
5.4 Selection of the most promising energy policies
65
Chart: Ranking of measures
| Industrial Process improvement | Ecomovil | Renewal of industrial equipment | Change of energy vector | Municipal Transport Reposition | Improvement of Industrial buildings | Improving the insulation of municipal buildings | Network of EV recharching points | Improvement of municipal lighting | Promoting public transport | Heating, ventilation and air-conditioning systems | Cycling Routes | Information stands | Introduction of renewable energies and self-consumption
Ideals | 0.037109 | 0.043001 | 0.045043 | 0.053888 | 0.064789 | 0.08546 | 0.089333 | 0.13905 | 0.14341 | 0.22139 | 0.24981 | 0.2591 | 0.33383 | 1
The results can be exported and more visual graphs can be obtained.

## Slide 66
UNIT 6
CASE STUDIES USING THE MONITORING TOOL
MOOC 2: Energy transition measurement and monitoring tools
66

## Slide 67
UNIT 6. CASE STUDIES USING THE MONITORING TOOL
1
Introduction to case studies
2
Case study in Spain
3
Case study in Italy
4
Case study in Greece
INDEX
67

## Slide 68
Purpose
This unit presents real-world case studies demonstrating the application of the GENERA Monitoring Tool in various contexts.
Learning Objectives
Understand how the tool is used in practice, interpret results, and apply insights to different scenarios.
Outcome
Gain practical knowledge on using the GENERA tool for energy transition planning and monitoring in diverse settings.
6.1 Introduction to Case Studies
Case Studies
The case studies to be evaluated are located on the island of Ibiza (Spain), Sardinia (Greece) and Rhodes (Greece).
Ibiza (Spain)
Sardinia (Italy)
Rhodes (Greece)
68

## Slide 69
6.2 Case Study 1: Ibiza (Spain)
69
Study of the Spanish National Context
Data entered in the tool take 2022 as the reference year (since 2023 is incomplete for some sectors) (International Energy Agency).
Oil is the main source in the transport sector and in other sectors such as agriculture, fishing, etc. On the other hand, natural gas is more involved in the industry, residential and service sectors. In addition, in electricity production, natural gas and renewables are the main producers.
Application of GENERA's energy planning tool
GENERA tool
Reference Data
Energy Balance

## Slide 70
6.2 Case Study 1: Ibiza (Spain)
70
Study of the Spanish National Context
Spain's energy context is characterized by the use of oil mainly for the transport sector, which in turn generates most of the country's emissions. There is a growing trend towards the use of renewable energy, mainly for electricity production, but also for residential use.
Natural gas also shows a growing trend and greater involvement in the industrial, residential and service sectors.
In terms of emissions, the most damaging sector is transport, followed by electricity generation.

## Slide 71
Context
Located in the northwest of the island of Ibiza. The municipality has an area of 12,662 hectares and a population of 27,431 inhabitants.
After signing the Covenant, it should consider “the adaptation of structures including the allocation of adequate human and economic resources” as a formal commitment
Challenges
It has set the promotion of renewable energies so that they represent at least 32% of the energy consumption of the municipality in the year 2030.
Increase the city's energy efficiency by 32.5% by the year 2030, with respect to 2005 energy consumption.
The global emissions reduction target for the year 2030 represents a reduction of 63,838.23 tons of CO2.
6.2 Case Study 1: Ibiza (Spain)
71
Summary of actions of Sant Antoni de Portmany (Ibiza)
GENERA tool
Application of the GENERA inference module.

## Slide 72
Actions
6.2 Case Study 1: Ibiza (Spain)
72
Summary of actions of Sant Antoni de Portmany (Ibiza)
Municipal Buildings And Public Facilities
Indoor lighting renovation
Substitution Of Lights For More Efficient Ones
Installation of aerothermal energy in municipal facilities
Photovoltaic solar energy installations
Replacement of municipal vehicles with more efficient ones
The main actions included in the generation tool are as follows

## Slide 73
Actions
6.2 Case Study 1: Ibiza (Spain)
73
Summary of actions of Sant Antoni de Portmany (Ibiza)
Increase of cycling routes
Network of EV recharging points
Measures to promote public transport and reduce private vehicle use
Transport
Awareness
Awareness-raising information stands

## Slide 74
6.2 Case Study 1: Ibiza (Spain)
74
Multicriteria Decision in Sant Antoni
Considering the priorities established by the municipality, the criteria used to prioritize the different levels are as follows:
Raise awareness and educate citizens about climate change.
Promote energy efficiency and the use of renewable sources.
Encourage responsible resource management
Design a sustainable and efficient municipality
GENERA tool
Application of the multi-criteria module and software SuperDecisions
Municipal priorities

## Slide 75
6.2 Case Study 1: Ibiza (Spain)
75
Results
Chart: Ranking of measures in Sant Antoni
| Improvement of Industrial buildings | Industrial Process improvement | Renewal of industrial equipment | Improvement of municipal lighting | Change of energy vector | Ecomovil | Improving the insulation of municipal buildings | Municipal Transport Reposition | Promoting public transport | Network of EV recharching points | Information stands | Cycling Routes | Introduction of renewable energies and self-consumption | Heating, ventilation and air-conditioning systems
Ideals | 0.046147 | 0.046932 | 0.05169 | 0.15219 | 0.16558 | 0.1962 | 0.27326 | 0.29674 | 0.40997 | 0.41686 | 0.449 | 0.56255 | 0.91178 | 1

## Slide 76
6.3 Case Study 2: Sardinia (Italy)
76
Data entered in the tool take 2022 as the reference year (since 2023 is incomplete for some sectors) (International Energy Agency).
The use of fossil fuels such as oil, mainly for the transport and agriculture/fishing sectors, and natural gas for the industrial, residential and services sectors, as well as for electricity generation, are particularly relevant. In addition, renewables are also especially significant in the residential sector
Application of GENERA's energy planning tool
GENERA tool
Reference Data
Energy Balance
Study of the Italian National Context

## Slide 77
6.3 Case Study 2: Sardinia (Italy)
77
Italian energy context is characterized by the use of natural gas and oil mainly, whose major contribution is divided between the transport and electricity generation sectors. Renewable energies are more involved in the residential and electricity sectors and there is a growing trend mainly for electricity production.
Natural gas also shows a growing trend and greater participation in the industrial, electricity generation, residential and services sectors.
The most damaging sector in term of emissions is electricity generation, followed by transport.
Study of the Italian National Context

## Slide 78
Context
Stintino is a town in the Italian province, region of Sardinia, with 1,212 inhabitants.
The municipality of Stintino joined the Covenant of Mayors initiative with the main objective of reducing CO2 emissions by 20%.
Challenges
Actions planned in relation to new buildings and the increase of existing buildings with higher performance.
Improvement of accessibility conditions in the urban area: transportation methods, bicycle lanes and pedestrian areas.
Reduced dependence on conventional energy sources.
Implementation of awareness, training and citizen participation processes to improve sustainability and education in terms of energy consumption.
6.3 Case Study 2: Sardinia (Italy)
78
Summary of actions of Stintino (Sardinia)
Application of the GENERA inference module.
GENERA tool

## Slide 79
6.3 Case Study 2: Sardinia (Italy)
79
Summary of actions of Stintino (Sardinia)
Actions
Municipal Buildings And Public Facilities
Improving energy efficiency in municipal buildings
Substitution Of Lights For More Efficient Ones
Improvement of building conditioning
Introduction of renewable energies in public buildings
Replacement of municipal vehicles with more efficient ones
The main actions included in the generation tool are as follows

## Slide 80
6.3 Case Study 2: Sardinia (Italy)
80
Summary of actions of Stintino (Sardinia)
Actions
Increase of cycling routes
Network of EV recharging points
Measures to promote public transport and reduce private vehicle use
Industry
Transport
In the tertiary and productive sector, measures and promotion of environmental management tools are also introduced to improve industrial buildings.

## Slide 81
6.3 Case Study 2: Sardinia (Italy)
81
Summary of actions of Stintino (Sardinia)
Actions
Awareness
This category includes raising public awareness, creating communication and awareness plans, workshops for schools and energy consumption reduction strategies.
In addition, discount rates for sustainable bioclimatic constructions are also proposed.

## Slide 82
6.3 Case Study 2: Sardinia (Italy)
82
Multicriteria Decision in Stintino
Considering the priorities established by the municipality, the criteria used to prioritize the different levels are as follows:
Adapt the municipality's public facilities.
Involve civil society to develop and improve the action plan with citizen awareness.
Reduce energy consumption through actions in municipal buildings.
Inclusion of PV systems in buildings and land in the municipality, as well as promoting their installation at the individual level.
Development of heating with cogeneration plants.
GENERA tool
Application of the multi-criteria module and software SuperDecisions
Municipal priorities

## Slide 83
6.3 Case Study 2: Sardinia (Italy)
83
Results
Chart: Ranking of measures in Stintino
| Industrial Process improvement | Ecomovil | Renewal of industrial equipment | Municipal Transport Reposition | Change of energy vector | Improvement of Industrial buildings | Improving the insulation of municipal buildings | Network of EV recharching points | Improvement of municipal lighting | Promoting public transport | Heating, ventilation and air-conditioning systems | Information stands | Cycling Routes | Introduction of renewable energies and self-consumption
 | 0.036993 | 0.046046 | 0.05013 | 0.07108 | 0.075465 | 0.10098 | 0.12188 | 0.15364 | 0.15777 | 0.17904 | 0.22345 | 0.26398 | 0.28035 | 1

## Slide 84
6.4 Case Study 3: Halki (Greece)
84
Data entered in the tool take 2022 as the reference year (since 2023 is incomplete for some sectors) (International Energy Agency).
High presence of oil in all sectors, although it stands out mainly in the transport sector, and others such as agriculture and fisheries. Natural gas is most involved in electricity generation, followed by the industrial and residential sectors. Renewable energies are also producers of electricity and have a great impact on the residential sector
Application of GENERA's energy planning tool
GENERA tool
Reference Data
Energy Balance
Study of the Greek National Context

## Slide 85
6.4 Case Study 3: Halki (Greece)
85
The Greek energy context is mainly characterized by the use of oil and natural gas in sectors such as transport and agriculture and fishing.
Renewable energies are more involved in the residential and electricity sectors. There is a growing trend in the use of renewable energies, mainly for electricity production.
The sector that emits the most emissions is the electricity generation sector due mainly to coal, and it is followed by transport.
Study of the Greek National Context

## Slide 86
Context
Smallest inhabited island of the Dodecanese with an area of 28 km2. It is part of the regional unit of Rhodes. It has a permanent population of 330 inhabitants (increasing during the summer months).
Challenges
It has a large photovoltaic park and the installation of solar energy facilities is planned. It is estimated that the island's energy needs can be covered.
The municipality has set itself the target of reducing CO2 by 105% by 2030, which exceeds the required 40% by far, so the emissions must be very demanding.
6.4 Case Study 3: Halki (Greece)
86
Application of the GENERA inference module
GENERA tool
Study of the Greek National Context

## Slide 87
6.4 Case Study 3: Halki (Greece)
87
Actions
Municipal Buildings And Public Facilities
Improving energy efficiency in municipal buildings
Substitution Of Lights For More Efficient Ones
Improvement of building conditioning
Introduction of photovoltaic solar energy for power production
Replacement of municipal vehicles with more efficient ones
The main actions included in the generation tool are as follows
Summary of actions of Halki (Greece)

## Slide 88
6.4 Case Study 3: Rhodes (Greece)
88
Actions
Increase of cycling routes
Promoting public transport
Transport
Awareness
Implementation of Ecomovil
Awareness-raising information stands
Summary of actions of Halki (Greece)

## Slide 89
6.4 Case Study 3: Halki (Greece)
89
Multicriteria Decision in Halki
Considering the priorities established by the municipality, the criteria used to prioritize the different levels are as follows:
Promotion of recycling and organics reduction.
Energy audit in municipal buildings.
Information to users to improve the behaviour and optimal use of the different equipment.
Substitution of LED lamps in lighting systems.
Development of heating with cogeneration plants.
GENERA tool
Application of the multi-criteria module and software SuperDecisions
Municipal priorities

## Slide 90
6.4 Case Study 3: Halki (Greece)
90
Results
Chart: Ranking of measures in Halki
| Industrial Process improvement | Renewal of industrial equipment | Ecomovil | Change of energy vector | Municipal Transport Reposition | Improvement of Industrial buildings | Improving the insulation of municipal buildings | Network of EV recharching points | Improvement of municipal lighting | Promoting public transport | Cycling Routes | Heating, ventilation and air-conditioning systems | Information stands | Introduction of renewable energies and self-consumption
Ideals | 0.034254 | 0.041196 | 0.046054 | 0.05519 | 0.067386 | 0.092842 | 0.093977 | 0.13344 | 0.1494 | 0.23012 | 0.26884 | 0.26897 | 0.39276 | 1

## Slide 91
Key Lessons from Case Studies
Purpose of the GENERA Tool
Modular and Tailored Approach
The tool includes different modules, allowing qualitative data integration for better adaptability to smaller municipalities.
Comprehensive Data Management
It provides precise context through national, regional, and local data, helping policymakers set clear sustainability goals.
Usability and Future Improvements
Designed to be user-friendly but could benefit from enhancements, such as a manual and improved information visibility.
Pilot Testing and Expansion
91
Developed to assist municipalities, particularly on islands, in creating energy transition action plans with national, regional, and local insights.
Tested in several island municipalities in Spain, Italy, and Greece, yielding energy-saving measures and CO2 reductions, with plans for further refinement and expansion

## Slide 92: MOOC 2 Energy transition measurement and monitoring tools